## Slide 1: 3D Natural user interface using Kinect
LUCCIN Karim – LUONG Kevin

## Slide 2: Summary
Motivations
Background
Objectives
Solution
Theory/Technical
Results
Conclusion

## Slide 3: Motivations
Interested in new kinds of experience for the user:
  Games
  Devices
“Boom” of touch devices

## Slide 4: Background
« Touch screen era »
New way to interact with computer
General public doesn't use the Kinect as a camera but only as a gaming device

## Slide 5: Objectives
Discover the possibilities and limits offered by the Kinect
Provide a new experience for the user
  Web browser using hands as Mouse cursor
  Media center

## Slide 6: Solution
Must be responsive : running in Real Time (30 frames per sec)
Able to be bound with 3D window system

## Slide 7: Solution
Considering Kinect’s limitations:
  Distance
  Accuracy
  Recognition

## Slide 8: Theory Recognizing hand
Kinect Output : Depth, Video and Skeleton
  The algorithm requires only depth data
Pixels are filtered based on their distance from the sensor and grouped by blobs because closest blobs are more likely to be hands
The N biggest blobs are tracked by the software as potential hands candidates
Notes: Explains that the hands are used to control cursors
On utilise que le channel depth parce que la video n’est pas pratique et que squelette est moisi quand on est assis

## Slide 9: Technical Running in real time
Everything must run at 30 fps to match Kinect’s Speed (approx. 33ms for everything)
  Using the horsepower of the graphic card when possible (only simple tasks done on the CPU)
  The 3D scene is again rendered and composed on the graphic card

## Slide 10: Technical CPU vs GPU
Chart: 
| 4096 x 1024 | 2048 x 512 | 1024 x 256 | 512 x 128 | 256 x 64 | 128 x 32
CPU | 4.2019 | 1.0631 | 0.28387 | 0.153 | 0.049843 | 0.038114
GPU | 3.46e-05 | 3.4e-05 | 3.07e-05 | 5.77e-05 | 3.33e-05 | 3.46e-05
Seconds
Used range
Notes: 4096 x 1202
CPU : 4.2019180
GPU : 0.0000346
2048 x 600
CPU : 1.0630711
GPU : 0.0000340
1024 x 300
CPU : 0.2838696
GPU : 0.0000307
512 x 150
CPU : 0.1529975
GPU : 0.0000577
256 x 74
CPU : 0.0498430
GPU : 0.0000333
128 x 36
CPU : 0.0381143
GPU : 0.0000346

## Slide 11: Technical Implemented algorithm
Kinect depth acquisition (CPU - Driver)
Depth filtering and scaling (GPU)
Region extracting (GPU)
Borders gradients (GPU)
Blobs counting and directions approximation (CPU)
Tracking of the N main Blobs (CPU)
Gesture recognition and web pages rendering (CPU)
Final composition for the UI (GPU)
Notes: Dire que les 5 premières étapes sont les plus importantes du point de vue real time, et dire ensuite que je vais l’expliquer en détail dans le slide suivant

## Slide 12
Original Kinect Depth Image
Regions extraction
Borders gradients
Filtered Depth
Final data : blobs + borders + orientation
Notes: Mettre des légendes
Expliquer que la main est obtenue à partir de la distance et de l’orientation des blobs

## Slide 13: Results
Total Time of the Algorithm : 10 – 18 ms
Dire aussi ce qui se passe si on utilise que 2 blobs et pas 4, ou 6, etc. Genre un graph recognition rate en fonction du nb de blobs

## Slide 14: Conclusion
Features offered by the Kinect
  Depth data
  Color data
  Skeleton recognition
Limitations
  Distance
  Accuracy when not standing up
“Easy-to-use” camera
PC Kinect in development Minimum Depth : 50 cm (1m with the current Kinect)
Notes: Mettre les specs « rumors » de la Kinect 2 (pour le fun)

## Slide 15: Thank you for your attention