## Slide 1: 3D Natural user interface using Kinect
LUCCIN Karim – LUONG Kevin

## Slide 2: Summary
Motivations
Background
Objectives
Implemented solution
Theory/Technical
Results
Conclusion

## Slide 3: Motivations
Interested in new kinds of experience for the user:
  Games
  Devices
“Boom” of touch devices

## Slide 4: Background
New way to interact with computer
« Touch screen era »
General public doesn't use the Kinect as a camera but only as a gaming device

## Slide 5: Objectives
Discover the possibilities and limits offered by the Kinect
Provide a new experience for the user
  Web browser
  Media center

## Slide 6: Implemented Solution
Must be responsive : running in Real Time
Able to be bound with 3D rendering (via DirectX 9)

## Slide 7: Implemented Solution
Considering limitations due to distance, accuracy, recognition…

## Slide 8: Theory
The algorithm requires only depth data from the Kinect
Pixels are filtered based on their distance from the sensor and grouped by blobs
The 4 biggest blobs are tracked by the software as potential cursors

## Slide 9: Technical
Everything must run at 30 fps to match Kinect’s Speed (approx. 33ms for everything)
Using the horsepower of the graphic card when possible (only simple tasks done on the CPU)
The 3D scene is again rendered and composed on the graphic card

## Slide 10: Technical
Kinect depth acquisition (CPU - Driver)
Depth filtering and scaling (GPU)
Region extracting (GPU)
Borders gradients (GPU)
Blobs counting and directions approximation (CPU)
Tracking of the 4 main Blobs (CPU)
Gesture recognition and web pages rendering (CPU)
Final composition for the UI (GPU)
Total Time : 10 – 18 ms

## Slide 12: Results
Demonstration Web browser

## Slide 13: Conclusion
Features offered by the Kinect
  Depth data
  Color data
  Skeleton recognition
Limitations
  Distance
  Accuracy when not standing up
“Easy-to-use” camera
Kinect 2 in development

## Slide 14: Thank you for your attention